## Slide 1: Networking
Marquette University
Fall 2021

## Slide 2: Waves
Dynamic (sine-shaped) wave
  Period T
  Frequency measured in herz = 1/second
period T
peak amplitude
amplitude
time

## Slide 3: Waves
Phase:
  Amount of shift in forward direction needed to align to sine wave
  Orange: Phase is zero
  Blue: Phase is -T/6 or -60° = 300°
  Green: Phase is T/6 or 60°
T/6

## Slide 4: Exercises
The period of a sine wave is 60 msec. What is the frequency?
Electricity in the US has a frequency of 60 hz. What is the period?

## Slide 5: Waves
Waves propagate in a medium
During one period, the wave progresses by a wavelength λ
In vacuum, propagation speed is the speed of light, or
General formula:
At time t
At time t+T
wavelength

## Slide 6: Waves
Period:
Wavelength given by speed times travel time:
Therefore

## Slide 7: Exercises
Blue light has a frequency of about 650 Thz =
What is its wavelength in micrometers?

## Slide 8: Exercises
Blue light has a frequency of about 650 Thz = hz.
What is its wavelength in micrometers in a coaxial cable. The propagation speed in a coax is two thirds of that in a vacuum.

## Slide 9: Exercises
The speed of sound is 343 m / sec (on a nice day). The standard A is 440 hz. What is the wavelength?
Half a wavelength is used for wind instruments

## Slide 10: Time Frequency Domain
Fourier Analysis

## Slide 12: Time - Frequency Domain
If we disregard phase, then a sine-wave is determined by its frequency and peak amplitude
Peak amplitude is 5, Frequency is 7 hz. (Interval is from 0 to 2.0)

## Slide 13: Time - Frequency Domain
Frequency Domain
Gives the amplitude for the frequency
A simple sine wave corresponds to a single spike

## Slide 14: Time-Frequency Domain
Three functions with different frequencies and their frequency graph

## Slide 15: Time Frequency Domain
We superimpose these functions

## Slide 16: Fourier Analysis
Any well-behaved periodic function can be written as a sum of sine functions with different frequencies, amplitudes, and phases
  Assume a periodic function
    Periodic means
    We pick without loss of generality

## Slide 17: Fourier Analysis
Then
  with

## Slide 18: Fourier Analysis
Note that the sine is just the cosine with a phase difference of 90°
  Peak amplitude is therefore just

## Slide 19: Fourier-Analysis Example
Example:
  Use periodicity to extend definition to all real numbers

## Slide 20: Fourier Analysis Example
Constant member of Fourier series is
  Of course, frequency 0 means a constant current
  (This is actually a problem for signaling from one node to another because you are using up energy.)

## Slide 21: Fourier Analysis Example
The sine components are all zero
This is because the function is even:

## Slide 22: Fourier Analysis Example
First cosine coefficient is
First partial Fourier series is
  (Negative cos is just the cos at a phase of 180°)

## Slide 23: Fourier Analysis Example
Second cosine coefficient is
Second partial Fourier series is

## Slide 24: Fourier Analysis Example
List of cosine coefficients is -0.569667, -0.0968758, -0.0965755, -0.0386943, -0.0428448, -0.0221663, -0.0252003, -0.0148282, -0.0169907, -0.0108211, …
10th partial Fourier sum gives a somewhat shaky approximation

## Slide 25: Fourier Analysis Example
We can use the coefficients to translate this function to the frequency domain

## Slide 26: Fourier Analysis Example
A simpler example is the square wave
Evaluating the integrals, we obtain

## Slide 27: Fourier Analysis Example
Notice Gibb’s phenomenon: Ringing near discontinuities

## Slide 28: Fourier Analysis Examples
Spectograms:
  Audio signal
    Break into short intervals
    Display Fourier transform per interval
    Bear growling

## Slide 29: Fourier Analysis Examples
Spectograms:
  Audio signal
    Break into short intervals
    Display Fourier transform per interval
    Monkey being a monkey

## Slide 30: Fourier Analysis
To transmit signals, we need more than a single sine wave
A composite signal is a combination of simple sine waves with different frequencies
  Periodic signals can be decomposed into series of simple sign waves with discrete frequencies
  An aperiodic signal can be decomposed into a combination of an infinite number of simple sine waves

## Slide 31: Fourier Analysis
Why is this important:
  Carriers offer different attenuation to different frequencies
We want to understand how carriers can subdivide their spectrum

## Slide 32: Non-periodic Signals
In reality, signals are not periodic
  We can make them periodic by repeating the pattern at larger and larger distances

## Slide 33: Non-periodic signals
As the period gets bigger and bigger
  Frequency domain graph becomes closer and closer to continuous function

## Slide 34: Non-periodic signal
Time Domain
Frequency Domain
4 kHz

## Slide 35: Non-periodic Signal
Human voice has a continuous range of 20 to 10,000 Hz
  Needs 100 to 4000 Hz to be understandable

## Slide 36: Bandwidth of Physical Links

## Slide 37: Physical Links
Any analog signal can be represented with a Fourier series for a limited time
  Fourier series technique important because medium or electronics can limit frequencies transmitted

## Slide 38: Bandwidth
Range of frequencies in a composite signal is bandwidth
  Difference between highest and smallest frequency
    Example:
    Here: Bandwidth is 600 Hz, not 700 Hz

## Slide 39: Bandwidth
Periodic signal
  Bandwidth contains all integer frequencies between the lowest and the highest frequency
Non-periodic signal
  Bandwidth contains all frequencies between the lowest and the highest frequency

## Slide 40: Bandwidth
AM radio station in US has a bandwidth of 10 kHz
  Total AM radio range is from 530 kHz to 1700 kHz
  Bandwidth chosen to allow for good human speech transmission
FM radio station in US has a bandwidth of 200 kHz
  FM spectrum ranges from 88 to 108 Mhz

## Slide 41: Bandwidth
Analog black-and-white TV
  Screen made up of pixels that are either black or white
  Screen is scanned 30 times / sec
  Resolution is 525 ⨉ 700 for 367,500 pixels
  Need 367,500 ⨉ 30 = 11,025,000 pixels
  Worst case scenario is alternating black and white pixels
  Represent one color by minimum, other by maximum amplitude
  Allows us to send 2 pixels per cycle
  Need 11,025,000/2 = 5,512,500 cycles per second or 5.512 MHz
  Best case is all one color, with frequency 0
  Therefore, bandwidth needed is 5.512 MHz

## Slide 42: Digital Signals

## Slide 43: Digital Signals
Digital signals have few signal levels
  Two signal levels zero and one
  20 bits sent per second
  bit-rate is 20bps

## Slide 44: Digital Signals
Four signal levels
40 bits sent per second
  40 bps

## Slide 45: Digital Signals
The number of signal levels needed to send bits per time unit is
Reversely: With signal levels, can send bits per time unit

## Slide 46: Digital Signals
Group exercise:
  We download text documents at 100 pages per second
  What is the bit rate needed?

## Slide 47: Digital Signals
Group exercise answer:
  Assume 30 lines with 80 characters per line
  Each character requires 8b
  Per second, we download
    bits
    Or 1.92 Mbps

## Slide 48: Digital Signals
To be recognizable, human voice needs a 4-kHz bandwidth analog signal
What is the bit rate?
  We need to sample at twice the highest frequency
  Each sample takes 8 bits

## Slide 49: Digital Signals
To be recognizable, human voice needs a 4-kHz bandwidth analog signal
What is the bit rate?
  We need to sample at twice the highest frequency
  Each sample takes 8 bits

## Slide 50: Bit Length
Digital equivalent to wavelength
  Distance one bit occupies on the transmission medium
    bit length
    propagation speed
    bit duration

## Slide 51: Nature of Digital Signals
Digital signal is non-periodic, so it has an infinite bandwidth (using Fourier Analysis)
Example: A single pulse

## Slide 52: Transmission of Digital Signals
Baseband transmission:
  Sends the digital signal over a channel without changing the digital signal to an analog signal
  Needs a low-pass channel
    A channel with bandwidth that starts from zero
    Example: Use a dedicated cable between two computers
    Example: Connect several computers to a bus, but have only one computer send at a time

## Slide 53: Transmission of Digital Signals
Baseband transmission:
  The digital signal is not distorted if the low-pass channel has infinite bandwidth
  Otherwise:
    Signal is distorted

## Slide 54: Transmission of Digital Signals
Broadband transmission:
  We change the digital signal to an analog signal for transmission
  This allows us to use a bandpass channel
    A channel where bandwidth does not start from zero

## Slide 55: Transmission Impairment

## Slide 56: Causes of Impairment
Attenuation: Loss of energy
Distortion: Signal changes its form
Noise: Other sources add to the signal

## Slide 57: Attenuation
Measured in decibel (dB)
  Compares the relative strength of signals
  Signal power at two different locations
  If we use voltage (power is proportional to the square of voltage)

## Slide 58: Attenuation
Group Activity
A signal suffers an attenuation of -15 decibel. The original peak amplitude is 5V. What is the peak amplitude when it is received.

## Slide 59: Attenuation
Group activity
  A cable suffers an attenuation of -0.5 db per km. What is the power of a signal that is original 0.7 mW after 5 km.
  (This is why decibels use a logarithm, you can just multiply the length of the cable with the attenuation per km to get the attenuation of the whole cable)

## Slide 60: Attenuation

## Slide 61: Distortion
Signal changes its form or shape.
  Signal Fourier components can have their own propagation speed and the received composite signal can be different.
Result of big phase shift in the higher harmonics

## Slide 62: Noise
Noise: “random" noise is added to signal
  Thermal, induced, crosstalk, impulse (from lightning)
  Signal to Noise Ratio

## Slide 63: Noise
Activity
  The power of a signal is 10 mW and the power of the noise is 1 μW. What are the values for SNR and SNR-decibel?

## Slide 64: Data Rate Limits

## Slide 65: Nyquest Bit Rate
For a noiseless channel:
  Levels: number of signal levels
  Maximum bit rate =
Can increase the maximum bit rate by increasing the number of levels
  But there is a practical limit to how many levels can be sustained

## Slide 66: Nyquest Bit Rate
What is the maximum bit rate for two signal levels for a noiseless channel with a bandwidth of 3000 Hz?

## Slide 67: Shannon Capacity
In reality, all channels are noisy
  Shannon capacity for highest data rate
    Depends on the Signal Noise Ratio

## Slide 68: Shannon Capacity
If , then Shannon capacity is

## Slide 69: Shannon Capacity
Regular telephone line
  Has bandwidth of 3000 Hz (300 Hz to 3300 Hz)
  Signal to Noise ratio is .
  Shannon capacity is
To increase the bit rate, we need to increase the bandwidth of the line or improve the signal to noise ratio

## Slide 70: Shannon Capacity
Signal to Noise ratio is often given in decibel
If channel bandwidth is 2 MHz and SNR is 36 decibel:
  , so
  Maximum bandwidth is

## Slide 71: Shannon Capacity
We have a channel with bandwidth 1-MHz. SNR is 60.
What are appropriate bit rate and signal level?
  We use Shannon capacity to find the upper limit for the bit-rate:
  For reasonable performance, we try to achieve .
  Nyquist tells us:
    So, we choose signal levels

## Slide 72: Performance

## Slide 73: Performance
Bandwidth
  For analog data: in Hz
  For digital data: in bps
  Relationship will be discussed next week
  E.g.: Telephone subscriber line
    has bandwidth of
    and 56 000 bps

## Slide 74: Performance
Throughput
  How fast can we actually send data through a network
  Limited by bandwidth

## Slide 75: Performance
Latency (Delay)
  Latency consists of
    propagation time = distance / propagation speed
    transmission time = message size / bandwidth
    queuing time : time needed for each device to hold message before it can be processed
    processing delay

## Slide 76: Performance
Example:
  Interoceanic copper cable for a 5 MB message
    Assume bandwidth is 1Mbps
    Distance = 12000 km
    Propagation speed is

## Slide 77: Performance
Propagation time is
Transmission time is